## Slide 1: Sant Dnyaneshwar Shikshan Sanstha's Annasaheb Dange College of Engineering and Technology (ADCET), Ashta (An Empowered Autonomous lnstitute affiliated to Shivaji University, Kolhapur)
Department of Civil Engineering
2025-26
AirShield: An IoT-Enabled Indoor Air Quality Monitoring and Alert System
Group Members: | Roll Number: | URN:
Sumit Parihar | 24 | 23031138
Barsha Gupta | 25 | 23031139
Akshita Jha | 31 | 23101051
Pranav Bhale | 43 | 23011075

## Slide 2: INTRODUCTION
Proposed Solution:
AirShield: An IoT-based system for real-time indoor air quality monitoring.
Monitors CO₂, VOCs, PM2.5, temperature, and humidity.
Provides threshold-based alerts (LED, buzzer, SMS/Telegram).
Visualizes data on an interactive dashboard for quick awareness.
Uniqueness of Solution:
Low-cost and accessible for classrooms, hostels, and offices.
Provides real-time monitoring with simple predictive/alerting capability.
Combines IoT sensors + cloud dashboard + alert system in one compact solution.
Includes simple comfort/health indicator (green/yellow/red) — not just raw values.
Problem:
Indoor air pollution often goes unnoticed.
Causes: CO₂ buildup, VOCs, PM2.5, humidity fluctuations, poor ventilation.
Effects: headaches, fatigue, reduced productivity, respiratory issues.
Existing solutions are often expensive, reactive, or limited to commercial settings.

## Slide 3: PROBLEM STATEMENT AND SCOPE OF THE PROJECT
Problem Statement
Indoor air quality in educational spaces often deteriorates unnoticed, yet it strongly influences student health, concentration, and academic performance.
Poor ventilation causes a buildup of CO₂, PM2.5, and VOCs — leading to fatigue, headaches, and respiratory issues.
Existing solutions are expensive, reactive, and not suited for small indoor spaces.
There is a need for a low-cost, smart system that monitors and predicts air quality in real time.
Scope of the Project
The system focuses solely on indoor air quality monitoring for environments like classrooms, hostels, and offices.
It uses low-cost sensors and microcontrollers (ESP32/NodeMCU) to collect and transmit environmental data.
Cloud platforms (e.g., ThingSpeak/Firebase) are used for data storage and retrieval.
Includes a user-friendly dashboard and alert system but does not control hardware like purifiers or HVAC systems

## Slide 4: OBJECTIVES
Design and implement
To design and implement AirShield, an IoT-based indoor air quality monitoring system for classrooms, hostels, and small indoor spaces.
Measure
To continuously measure key parameters: CO₂, PM2.5, VOCs, temperature, and humidity.
Provide
To provide threshold-based alerts through LEDs, buzzers, and SMS/Telegram notifications when air quality is unsafe.
Display
To display real-time data and historical trends on an interactive dashboard for easy monitoring.

## Slide 5: Progress Till Now
Problem analysis and literature review completed
IAQ parameters finalized
System architecture designed
Dashboard concept designed
Cloud platform studied
Notification system implemented
Real time data transmission enabled

## Slide 6: Finalised IAQ Parameters
〖𝐂𝐎〗_𝟐
It is relevant for ventilation efficiency.
VOC’s
It is relevant for indoor chemical pollutants.
〖𝐏𝐌〗_(𝟐.𝟓)
It is relevant for respiratory health.
CO
Temperature
Humidity
It will be monitored as a toxicity indicator.
It is relevant for thermal comfort.
It is relevant for comfort and microbial growth.
Levels consistently above this suggest poor ventilation and require fresh air adjustments.
<1000 ppm.
**ASHRAE Ventilation Standard.
<300 ppb.
**WHO AQI Guidelines.
<40 µg/m³ (24-hour average).
**CPCB NAAQS.
<2.0 mg/m³ (8-hour average).
**CPCB NAAQS.
20.0°C to 23.6°C in winter.
**ASHRAE Thermal Comfort.
22.8°C to 26.1°C in summer.
30% to 65%.
**ASHRAE & WHO Comfort Range.
It is relevant for ventilation efficiency.
VOC’s
It is relevant for indoor chemical pollutants.
It is relevant for respiratory health.
CO
Temperature
Humidity
It will be monitored as a toxicity indicator.
It is relevant for thermal comfort.
It is relevant for comfort and microbial growth.
Levels consistently above this suggest poor ventilation and require fresh air adjustments.
<1000 ppm.
**ASHRAE Ventilation Standard.
<300 ppb.
**WHO AQI Guidelines.
<40 µg/m³ (24-hour average).
**CPCB NAAQS.
<2.0 mg/m³ (8-hour average).
**CPCB NAAQS.
20.0°C to 23.6°C in winter.
**ASHRAE Thermal Comfort.
22.8°C to 26.1°C in summer.
30% to 65%.
**ASHRAE & WHO Comfort Range.

## Slide 8: Working Flow
Data Collection Sensors capture air quality
Processing ESP32 processes data
Transmission Data sent to Cloud)
VisualizationDashboard displays data
Alerts Triggered when limits exceed

## Slide 9: Expected Output/Dashboard
Dashboard Features
Displays air quality parameters (CO₂, PM2.5, etc.)
Systtem status indication
Graph-based visualization of data
Simple and user-friendly interface
Enables decision-making (e.g., open windows, reduce crowd density)
User Interface
Simple and easy-to-understand layout
Designed for quick awareness

## Slide 10
Dashboard Visuals
Dashboard Mock**
Alert and Optimization**

## Slide 11: Future Work
Complete sensor integration Integrate all selected sensors with ESP32
1
Connect dashboard with live data Replace sample data with real-time inputs
2

## Slide 12: THANK YOU